## Slide 1: Garbage Monitoring System
Group- 29
1.Amit Sharma- 2011016
2.Praveen Sharma- 2011209
3.Deepak Kapoor- 2011189
4.Saurabh Joshi -2011259
5.Ratna Prakirana- 2011211
6.Chhattlal Sahu- 2011042

## Slide 2: Problem Definition
Garbage overflow is a very serious issue especially in India. It causes many health and environmental problems and destroys aesthetic value of the surroundings. Following are some critical issues related to ‘Garbage Overflow’.
Overflow of garbage due to inefficient system of garbage collection.
Street animals spill out garbage on the road.
Spilled out garbage halts the traffic in the area
Water gets mixed with garbage during rains.
Garbage on the road and remnant garbage causes foul smell.
Houseflies and mosquitoes breeding on the garbage causes diseases like malaria, dengue etc.
Overflowed garbage and garbage which spills out damages the aesthetic beauty of the place.

## Slide 3: Flow Chart

## Slide 4: Concept Generation
Concept
Advantages-
1.Automatic.
2.Manual support , in case of power failure.
Disadvantages-
1.Power required.

## Slide 5: Concept CAD Model
Concept number 5 , shown in previous slide , is preferred to be the final Concept.
Fig. CAD view of Concept

## Slide 6: Embodiment Design
S. NO. | COMPONENTS | FUNCTION
1. | Container | Use for garbage collection
2. | Container’s roof | Use for covering
3. | Basket | Opening and closing of garbage bin, To throw garbage
4. | 4-bar linkage | Mechanism for opening and closing of window
5. | Geared Motor | To operate 4 bar linkage
6. | Handle | To open Basket in case of power failure
7. | Hinges | For rotary motion.
8. | Bearing | Reduce friction between linkage
9. | Gate locking pin | For lock the back door
10. | At mega -16(micro controller) | For controlling various activity
11. | Back door | For taking out garbage
12. | Max-232(TTL logic convertor) | TTL Logic converter
13. | Gsm Module | For transmitting message
14. | IR Sensor | For checking Garbage is full or not
15. | Tsop Sensor module | To check vicinity of human
16. | L298 (motor driver) | To drive motor
17. | 7805 (Power regulator) | Power Regulator
18. | resistor and capacitor (.1Uf) | Parts of circuit
19. | Fecl3 | For etching
20. | Printed circuit board | To Print the circuit
21. | Adapter12V | For supplying power to circuit.
22. | Li-ion cell | For circuit operating
Product Architecture:

## Slide 7: Parametric design
Container
Coupler

## Slide 8: Continued…
Crank
Left Basket

## Slide 9: Continued…
Right Basket
Roof

## Slide 10: Prototype
Circuit design

## Slide 11: Prototype
Isometric View

## Slide 12: Circuit Design

## Slide 13: Standard Parts Vendors
S.no. | Name | Address
1. | Nex Robotics | Airoli , Mumbai
2. | Probots Techno Solutions | NagarBhavi Main Road ,Bangalore
3. | Robomart | Nithari Branch, Noida
4. | Bhavani Plywood | City Cofee House ,Jabalpur
5. | Mehta Electronics | Karam Chand Chowk , Jabalpur
6. | Robosystems | Online
7. | Gujrat Hardware | Jabalpur
Geared Motor(30 rpm)
Lever
Atmega -16
Back door
Max-232
Gsm Module
IR Sensor
Tsop Sensor
L298
7805
Register and capacitor (.1Uf)
Fecl3
Pcb
Adapter

## Slide 14: Fabrication

## Slide 15: Fabrication
Crank-rocker mechanism is used .Rocker angle is 45-50 degree. There are total 4-linkage in mechanism.Links are connected with revolute joints. Bearing are used to make bearing (internal Diameter = 10mm, External Diameter = 24mm).
Shaft is used to connect two bearing so revolute joint can be made.

## Slide 16: Fabrication
External View -
Window gets open once a person come to throw
the garbage.
Window gets closed automatically after few seconds.

## Slide 17: Ultrasonic sensors (mounted) to detect the presence of a person . Maximum range over which it can detect the presence is 3 meters and an angle of 15 0.
Fabrication
Components Used -
Ultrasonic Sensor send the message to the Arduino Atmega32 (controller) and controller actuates the motor and it give AT command to GSM to send message.

## Slide 18: Motor is fixed to side wall of bin and motor shaft is connected to crank of mechanism.The RPM of motor is 30 and torque is 5kg/cm. and operate at 10V , .5A current
Fabrication
Components Used -
Ultrasonic Sensor send the message to the Arduino Atmega32 (controller) and controller actuates the motor and it give AT command to GSM to send message.

## Slide 19: This IR sensor detects whether the garbage bin is full or not and it sends signal to the controller. The range is 6 cm
Fabrication
Components Used -
GSM SIM900A module receives the signal from the controller and then sends message to the respective authority.

## Slide 20
Product Analysis
Problems -
Sensor cannot differentiate between human beings and big animals.
Bearings need time to time maintenance.
Due to network problem some times alert message can not be send.
Future Scope -
The Dustbin can be made renewable by using lithium ion battery and sonar Panel. The Garbage Bin will the be operated by sunlight.